## Slide 1: Lecture 7: VHDL - Introduction
ELEC 2200: Digital Logic Circuits
Nitin Yogi (yoginit@auburn.edu)

## Slide 2: Introduction
Hardware description languages (HDL)
  Language to describe hardware
  Two popular languages
    VHDL: Very High Speed Integrated Circuits Hardware Description Language
      Developed by DOD from 1983
      IEEE Standard 1076-1987/1993/200x
      Based on the ADA language
    Verilog
      IEEE Standard 1364-1995/2001/2005
      Based on the C language

## Slide 3: Applications of HDL
Model and document digital systems
  Different levels of abstraction
    Behavioral, structural, etc.
Verify design
Synthesize circuits
  Convert from higher abstraction levels to lower abstraction levels

## Slide 4: Input-Output specification of circuit
my_ckt
A
B
S
X
Y
Example: my_ckt
  Inputs: A, B, C
  Outputs: X, Y
VHDL description: entity my_ckt is port (
A: in bit; B: in bit; S: in bit; X: out bit; Y: out bit); end my_ckt ;

## Slide 5: VHDL entity
my_ckt
A
B
S
X
Y
entity my_ckt is port ( A: in bit; B: in bit; S: in bit; X: out bit; Y: out bit ); end my_ckt;
Name of the circuit
User-defined
Filename same as circuit name
Example.
  Circuit name: my_ckt
  Filename: my_ckt.vhd
Port names or Signal names
Name of the circuit
User-defined
Filename same as circuit name recommended
Example:
  Circuit name: my_ckt
  Filename: my_ckt.vhd
Datatypes:
In-built
User-defined
Direction of port
3 main types:
in: Input
out: Output
inout: Bidirectional
Note the absence of semicolon “;” at the end of the last signal and the presence at the end of the closing bracket

## Slide 6: Built-in Datatypes
Scalar (single valued) signal types:
  bit
  boolean
  integer
  Examples:
    A: in bit;
    G: out boolean;
    K: out integer range -2**4 to 2**4-1;
Aggregate (collection) signal types:
  bit_vector: array of bits representing binary numbers
  signed: array of bits representing signed binary numbers
  Examples:
    D: in bit_vector(0 to 7);
    E: in bit_vector(7 downto 0);
    M: in signed (4 downto 0); --signed 5 bit_vector binary number

## Slide 7: User-defined datatype
Construct datatypes arbitrarily or using built-in datatypes
Examples:
  type temperature is (high, medium, low);
  type byte is array(0 to 7) of bit;

## Slide 8: Functional specification
Example:
  Behavior for output X:
    When S = 0 X <= A
    When S = 1 X <= B
  Behavior for output Y:
    When X = 0 and S =0 Y <= ‘1’
    Else Y <= ‘0’
my_ckt
A
B
S
X
Y

## Slide 9: VHDL Architecture
VHDL description (sequential behavior): architecture arch_name of my_ckt is begin p1: process (A,B,S)
begin
if (S=‘0’) then
X <= A;
else
X <= B;
end if;
if ((X = ‘0’) and (S = ‘0’)) then
Y <= ‘1’;
else
Y <= ‘0’;
end if;
end process p1; end;
Error: Signals defined as output ports can only be driven and not read

## Slide 10: VHDL Architecture
architecture behav_seq of my_ckt is
signal Xtmp: bit;
begin p1: process (A,B,S,Xtmp)
begin
if (S=‘0’) then
Xtmp <= A;
else
Xtmp <= B;
end if;
if ((Xtmp = ‘0’) and (S = ‘0’)) then
Y <= ‘1’;
else
Y <= ‘0’;
end if;
X <= Xtmp;
end process p1;
end;
Signals can only be defined in this place before the begin keyword
General rule: Include all signals in the sensitivity list of the process which either appear in relational comparisons or on the right side of the assignment operator inside the process construct. In our example: Xtmp and S occur in relational comparisons
A, B and Xtmp occur on the right side of the assignment operators

## Slide 11: VHDL Architecture
VHDL description (concurrent behavior):
architecture behav_conc of my_ckt is
signal Xtmp: bit;
begin
Xtmp <= A when (S=‘0’) else
B;
Y <= ‘1’ when ((Xtmp = ‘0’) and (S = ‘0’)) else
‘0’;
X <= Xtmp;
end ;

## Slide 12: Signals vs Variables
Signals
  Signals follow the notion of ‘event scheduling’
  An event is characterized by a (time,value) pair
  Signal assignment example:
    X <= Xtmp; means
    Schedule the assignment of the value of signal Xtmp to signal X at (Current time + delta)
    where delta: infinitesimal time unit used by simulator for processing the signals

## Slide 13: Signals vs Variables
Variables
  Variables do not have notion of ‘events’
  Variables can be defined and used only inside the process block and some other special blocks.
  Variable declaration and assignment example:
  process (…)
  variable K : bit;
  begin
  …
  -- Assign the value of signal L to var. K immediately
  K := L;
  …
  end process;
Variables can only be defined and used inside the process construct and can be defined only in this place

## Slide 14: Simulation
Simulation is modeling the output response of a circuit to given input stimuli
For our example circuit:
  Given the values of A, B and S
  Determine the values of X and Y
Many types of simulators used
  Event driven simulator is used popularly
  Simulation tool we shall use: ModelSim
my_ckt
A
B
S
X
Y

## Slide 15: Simulation
architecture behav_seq of my_ckt is
signal Xtmp: bit;
begin p1: process (A,B,S,Xtmp)
variable XtmpVar: bit;
begin
if (S=‘0’) then
Xtmp <= A;
else
Xtmp <= B;
end if;
if ((Xtmp = ‘0’) and (S = ‘0’)) then
Y <= ‘1’;
else
Y <= ‘0’;
end if;
X <= Xtmp;
XtmpVar := Xtmp;
end process p1;
end;
Time ‘T’ | A | B | S | Xtmp | Y | XtmpVar | X
0- | U | U | U | ‘X’ | ‘X’ | ‘X’ | ‘X’
0 | 0 | 1 | 0 | ‘X’ | ‘X’ | ‘X’ | ‘X’
0+d | 0 | 1 | 0 | 0 | 0 | 0 | ‘X’
0+2d | 0 | 1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0 | 1 | 0 | 0
1+d | 0 | 1 | 1 | 1 | 0 | 0 | 0
1+2d | 0 | 1 | 1 | 1 | 0 | 0 | 1
Scheduled events list: Xtmp = (0,0+d)
Y = (0,0+d)
X = (‘X’,0+d)
Assignments executed: XtmpVar = ‘X’
Scheduled events executed: Xtmp = 0
Y = 0
X = ‘X’
Assignments executed:
XtmpVar = 0
Scheduled events list: Xtmp = (0,0+2d)
Y = (1,0+2d)
X = (‘0’,0+2d)
Scheduled events executed: Xtmp = 0
Y = 1
X = 0
Scheduled events list: (empty)

## Slide 16: Synthesis
Synthesis: Conversion of behavioral level description to structural level netlist
  Abstract behavioral description maps to concrete logic-level implementation
  For ex. Integers at behavioral level mapped to bits at structural level
Structural level netlist
  Implementation of behavioral description
  Describes interconnection of gates
Synthesis tool we shall use: Leonardo Spectrum

## Slide 17: Structural level netlist
Behavior of our example circuit:
  Behavior for output X:
    When S = 0 X <= A
    When S = 1 X <= B
  Behavior for output Y:
    When X = 0 and S =0 Y <= 1
    Else Y <= 0
my_ckt
A
B
S
X
Y
Logic functions
  Sbar = ~ S
  Xbar = ~ X
  X = A*(Sbar) + B*S
  Y = (Xbar)*(Sbar)

## Slide 18: Structural level netlist
architecture behav_conc of my_ckt is -- component declarations
signal Sbar, Xbar, W1, W2: bit;
begin
G1: not port map(Sbar,S);
G2: and port map(W1,A,Sbar);
G3: and port map(W2,B,S);
G4: or port map(X,W1,W2);
G5: not port map(Xbar,X);
G6: and port map(Y,Xbar,Sbar);
end ;
Gate level VHDL descriptions (and, or, etc) are described separately
Design in which other design descriptions are included is called a “hierarchical design”
A VHDL design is included in current design using port map statement

## Slide 19: Other VHDL resources
VHDL mini-reference by Prof. Nelson
  http://www.eng.auburn.edu/department/ee/mgc/vhdl.html
VHDL Tutorial: Learn by Example by Weijun Zhang
  http://esd.cs.ucr.edu/labs/tutorial/